## Slide 1
Electrical
and Electronics science
First year
Computer Science and Engineering
Dr. Shakti Singh
ASSISTANT PROFESSOR
ELECTRCIAL AND INSTRUMENATION
ENGINEERING DEPARTMENT
@shakti.singh@thapar.edu

## Slide 2: Introduction
An Op Amp is an IC packaged into a single case to form a functional circuit.
Op Amp were primarily used to perform mathematical operations such as addition, subtraction, integration and differentiation, thus the term operational.

## Slide 3: Introduction
Operational amplifiers (op-amps) are among the most widely used building blocks in electronics
  they are integrated circuits (ICs)
    often DIL or SMT

## Slide 4
A single package will often contain several op-amps

## Slide 5: Background
Originally invented in early 1940s using vacuum tube technology
  Initial purpose was to execute math operations in analog electronic calculating machines
Shrunk in size with invention of transistor
Most now made on integrated circuit (IC)
  Only most demanding applications use discrete components
Huge variety of applications, low cost, and ease of mass production make them extremely popular

## Slide 6: Introduction
The internal structure of OpAmp is much more complex and consists of 20 transistors along with biasing resistors and capacitors.

## Slide 7: Operational Amplifier
Output gain high
  A ~= 106
Tiny difference in the input voltages result in a very large output voltage
  Output limited by supply voltages
Comparator
  If V+>V-, Vout = HVS
  If V+<V-, Vout = LVS
  If V+=V-, Vout = 0V

## Slide 8: 3-stage Op-Amp

## Slide 9: Equivalent Circuit
The amplifier’s differential inputs consist of a non-inverting input with voltage (V+) and an inverting input with voltage (V−). Ideally, an op-amp amplifies only the difference in voltage between the two, also called differential input voltage. The output voltage of the op-amp Vout is given by the equation:
Vout = AOL (V+ – V–)
Differential Amplifier
  Amplifies difference between inputs

## Slide 10: Why are they useful?
Sensor signals are often too weak or too noisy
  Op Amps ideally increase the signal amplitude without affecting its other properties

## Slide 11: Basic Operational Amplifier Circuits
Inverting and non-inverting amplifiers

## Slide 12: CHARACTERISTICS OF AN IDEAL OP- AMP
Infinite voltage gain A
Infinite input resistance Zin
Zero output resistance Zout
Zero output voltage when input voltage is zero
Infinite bandwidth
Infinite common mode rejection ratio so that the output common mode noise voltage is zero

## Slide 13: Ideal Op Amp vs Practical Opamp
Parameters | Ideal Op-Amp | Typical Op-Amp
Input Resistance | infinity | 106  (bipolar) 109  - 1012  (FET)
Input Current | 0 | 10-12 – 10-8 A
Output Resistance | 0 | 100 – 1000 
Operational Gain | infinity | 105 - 109
Common Mode Gain | 0 | 10-5
Bandwidth | infinity | Attenuates and phases at high frequencies (depends on slew rate)
Temperature | independent | Bandwidth and gain