## Slide 1
Electrical
and Electronics science
First year
Computer Science and Engineering
Dr. Shakti Singh
ASSISTANT PROFESSOR
ELECTRCIAL AND INSTRUMENATION
ENGINEERING DEPARTMENT
@shakti.singh@thapar.edu

## Slide 2: Field Effect Transistor
FETs are unipolar devices.
Two types of FETs Junction FET, Metal oxide semiconductor field effect transistor (MOSFET).
The term field effect relates to a depletion region formed in the channel of a FET as a result of voltage applied on one of its terminal.
FET is a voltage controlled device contrary to BJT, which is a current controlled device.

## Slide 3: JFET Construction

## Slide 4: JFET Operation
The JFET is always operated with gate source pn junction reverse biased.
The channel width and thus the channel resistance can be controlled by varying the gate voltage, thereby controlling the amount of drain current.
The junction is wider at the drain end because the reverse bias voltage between the gate and drain is greater than that between the gate and source.

## Slide 5: JFET Operation

## Slide 6: JFET Operation
Pinch off voltage: For VGS=0, the value of VDS at which ID becomes essentially constant is the pinch off voltage. At this value, the maximum drain current occurs and is known as IDSS.
Cut off voltage: The value of VGS that makes ID approximately zero is the cut off voltage.